## Slide 1: Distance Machine Locker
SP Digital Tech Talk (12 Jan 2017)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/distance-machine-locker

## Slide 2: Demo video
https://www.youtube.com/watch?v=mWyIHkdfHz4

## Slide 3: Problem?
Malicious person + unlocked machines
Solution:
  Distance-measuring system
  Locks machine when I leave

## Slide 4: System setup overview
Distance Sensor
Arduino Uno
OLED screen
(Debugging)
Mac Menubar app

## Slide 5: Hardware

## Slide 6: Active IR distance sensor
Sharp Infrared (IR) Distance Sensor GP2Y0A21YKR
Effective range: 10 to 80cm
Active IR
Less noisy than ultrasonic sensors
Source: http://education.rec.ri.cmu.edu/content/electronics/boe/ir_sensor/1.html

## Slide 7: Putting them all together
Arduino Uno in case meant for Mega 2560

## Slide 8: Host App
Swift 3 Menubar app
Receives Data from USB-Serial Port
Locks machine on threshold reached

## Slide 9: About the app
Uses SwiftSerial library written by yours truly
Menubar app (MainMenu.xib)
  No Main Window
  No Storyboards, just a single xib
Lock screen programmatically (Locking.swift)

## Slide 10: Potential Hacking Strategies and Defenses

## Slide 11: Hack 1: Disconnecting device
Defense:
  Lock machine immediately
  Issue system notification

## Slide 12: Hack 2: Tamper hardware to provide incorrect values
Defense:
Dynamic monitoring of distance values on menu bar
Requires “human” monitoring

## Slide 13: Hack 3: Reprogramming with malicious firmware
Defense: Reprogram Arduino before using it
Swift App contains hex (firmware) file
Flashes hex file to Arduino before using

## Slide 14: A possible “undetectable” hacking strategy
Overwrite the Arduino bootloader

## Slide 15: Typical Arduino Programming
Arduino IDE
USB cable

## Slide 16: Microcontroller programming the actual way
Using dedicated programmers with ICSP port
ICSP – In-circuit system programmer
Image sources:
http://www.atmel.com/tools/atatmel-ice.aspx
http://blog.alrightythen.de/2014/08/debugging-with-the-new-atmel-ice/
+
=

## Slide 17: What is an Arduino bootloader?
Allows Arduino IDE to program Arduino board via USB
On reset, wait 1 second for computer to program board before resuming

## Slide 18: Just pull me away from my desk to troll me
Hack 4:

## Slide 19: Hackers always win
No physical security -> No security
Questions?
https://github.com/yeokm1/distance-machine-locker